ZX14 Tiger Tail Inner Fender Installation Instructions

- Remove Seat and rear cowling plastic

- Remove Fuel Tank (remove fuel too. Tank will be heavy otherwise)

- Remove tool kit and tool kit plastic tray.

- Disconnect all electrical harness mounted to your stock inner fender and key latch for seat.

- Remove stock bolts connecting plastic inner fender to sub-frame.  (see reconnect pictures for locations)

- Transfer all rubber grommets and rubber collapse nuts to new Tiger Tail Inner Fender as shown.

- Cut square metal brace off of key latch as shown and mount key latch using supplied spacers.  Position back into sub-frame and connect rear of Inner Fender FIRST. See picture.  You MUST put aluminum mount plate ON TOP of black hole tabs.  NOT underneath.  You can loosen the 2 bolts securing the brace to position the aluminum mount plate to help, and then retighten when positioned.

- Now install the two mount bolts that secure the inner fender to the sub-frame along the cross brace.

- Replace your electrical harness and check all connectors.   You’re done.  Re-install Fuel Tank and all plastic cowling covers.